## Slide 1
Standard Works:
Swivel Chair
Meritage 3 seater
Sola Sofa
Douglas O'Keefe
06/18/2026

## Slide 2: Agenda
Understand Sola process and labor time
Review current state standard work procedures
  Cycle Time
  Theoretical Output
  Order of Operations
Operator Loading Chart by Task
Potential Improvements

## Slide 3: Key Takeaways: Swivel

## Slide 4: Improvements: Swivel

## Slide 5: Key Takeaways: Meritage
Meritage 3-seater Sofa assembly labor time: 254 min
Theoretical output based on cycle time (41.5 min), assuming parts are available from paint.
  ~10 units per day (7 operators)
  Takt time required (demand of 10 units): 42 min

## Slide 6: Improvements: Meritage
Assign different connector types part numbers. Currently, the 3 different types of Meritage connectors arrive the same way, and under 1 part #.
Eliminate connector screw swaps & reorientation: recovers ~11:40 of labor per unit to redeploy elsewhere
Pre-drill connector holes for screw entry: saves at least 6 min per frame assembly (seat-frame assembly is a top bottleneck)
Connectors pre-drilled 100% for leg pieces, and pre-drill mini-connectors where possible: improves every Meritage
Receive leg pieces pre-assembled from manufacturing: ~90% are built identically, so move that work upstream

## Slide 7: First Step to Pre-Assembly: Fix the Connector BOM
The first step to getting connectors pre-assembled in Vietnam: give each connector its own part number in the BOM.
Today the Meritage 3-Seater BOM lists 2 connector types — but there are really 3.
Location | Configuration | Part number | Qty
Front of frame | Type 1 (same both sides) | 1015301 | 2
Back – left | Left configuration | 1015302 | 1
Back – right | Right configuration | 1016592 | 1
The gap. The drawings already show all three connectors correctly — 1015301 (×2) on the front, and 1015302 + 1016592 on the back — but the BOM does not.
Fix this drawing-to-BOM mismatch first; then every connector can arrive from Vietnam pre-assembled to the correct configuration.

## Slide 8: Key Takeaways - Sola
Sola Lounge (No-Arm) Sofa assembly labor time: 124 min
Theoretical output based on cycle time (36.8 min), assuming parts are available from paint.
  ~11 units per day (4 operators)
  Takt time required (demand of 10 units): 42 min

## Slide 9: Operator Loading Chart by Task – Sola
0
12
24
36
48
2
3
4
5
36.8
S1
6
7
34.5
S2
8
33
S3
9
10
20.1
S4
Takt 42 min
Tasks (SWI step #)
#2 Rivet Nut Installation
#3 Connector Pre-Assembly
#4 Connector Plate Installation
#5 Connector Attachment
#6 Frame Sub-Assembly
#7 Frame Connection Assembly
#8 Seat Support Frame Assembly
#9 Trellis Frame Installation
#10 Corner Cap & End Cap
Takt 42 min · Cycle time 36.8 min · Capacity ~11 units/day · 84% line efficiency · Seat Support (#8, 33 min) is the bottleneck — splitting it 2-up unlocks more output.

## Slide 10: Improvements – Sola
Balance the line to takt: 4-station layout, every station under the 42-min takt (~11 units/day at ~84% efficiency)
Split the Seat Support / trellis assembly (#8, 33 min) the bottleneck; multiple slats make it parallelizable, so 2 builders unlock more output
Connectors delivered correct & pre-drilled (Connector Pre-Assembly + Plate + Attachment ≈ 28 min combined) cut prep and drilling time
Rivet nuts pre-installed by the supplier where possible (Rivet Nut Installation, #2)
Point-of-use storage / kit parts per unit to cut walking and fetching
Standardize cordless tools & batteries and stage a tool set at each station
Clearer quality standards to reduce wait time between assembly and packing approval