## Slide 1
TUUCI
STANDARD WORK · LINE-BALANCE STUDY
Meritage 3-Seater
Where the labor goes — and how we level it.
Findings from the standard-work data, with a proposed balanced line to meet a 10-unit/day demand.
1

## Slide 2
TUUCI
Meritage 3-Seater · Headlines
2
THE NUMBERS AT A GLANCE
One Meritage carries 254 minutes of hands-on work
Summed straight from the standard work instruction — 11 timed steps (the PPE step has no time).
254 min
Total labor per unit (4.24 labor-hours of hands-on work)
11
Timed work steps (SWI steps 2–12)
64 min
Biggest single step — Step 4, Arms Assembly (25% of the build)
61 %
of all labor sits in just 3 steps (Arms, Seat Frame, Back Frame)
Labor-hours vs. clock time. 254 min is total hands-on work — if one person built it alone. With a few builders working in parallel the wall-clock time per unit is much shorter; this study is about spreading those 254 minutes evenly so the line flows.

## Slide 3
TUUCI
Meritage 3-Seater · Bottlenecks
3
WHERE THE TIME CONCENTRATES
Three assemblies dominate — and each is bigger than takt
64
#4
47
#5
43.5
#6
22.5
#10
19.2
#2
18
#7
18
#11
8
#3
8
#9
5
#8
1
#12
takt 42 min
Bars = minutes per step (sorted). Gold line = cumulative %. Dashed = 42-min takt.
Step 4 — Arms Assembly: 64 min.
A quarter of the build, and 1.5× the takt by itself.
Step 5 — Seat Frame: 47 min and Step 6 — Back Frame: 43.5 min.
These three steps = 61% of the labor. Fix these and you move the line.
All three exceed the 42-min takt, so alone they cap output no matter how the rest is staffed.
Takt = 420 min (7 hr) ÷ 10 units = 42 min per unit — the pace we must match.

## Slide 4
TUUCI
Meritage 3-Seater · The Opportunity
4
WHERE WE CAN HELP
Put hands where the hours are
The three big assemblies are buildable in parallel — more than one person can work them at once. Splitting them is what brings every station under takt.
Step | Now | 2 builders
#4 Arms Assembly | 64 | 32
#5 Seat Frame Assembly | 47 | 23.5
#6 Back Frame Assembly | 43.5 | 21.8
Minutes per unit. Splitting helps only where the work is genuinely separable — these assemblies are.
The principle: a step’s labor doesn’t disappear when you split it — but the time on the clock drops, so it stops gating the line.
Arms (64 → 32) alone takes the worst bottleneck below takt.
Smaller steps (legs, attach, finishing, plate) are grouped to fill the remaining operators evenly.
Net effect (next slide): a level line that hits 10/day.

## Slide 5
TUUCI
Meritage 3-Seater · The Balance
5
THE LINE BALANCE
From lumpy to level
Today — work as it sits
Proposed — balanced to takt
2
19.2
#2
3
8
#3
4
64
#4
5
47
#5
6
43.5
#6
7
18
#7
5
#8
9
8
#9
10
22.5
#10
11
18
#11
1
#12
takt 42
2
3
27.2
S1
4
32
S2 ×2
5a
41
S3
5b
6a
39.5
S4
6b
7
9
41
S5
10
11
41.5
S6
takt 42
One operator per step: Arms towers at 64 min → a unit only every 64 min (~6.6/day), and small steps sit idle.
7 operators across 6 stations (Arms built 2-up; Seat & Back Frame split). Every station under takt → ~10.1/day, 88% utilized.

## Slide 6
TUUCI
Meritage 3-Seater · How it looks
6
HOW IT WOULD ACTUALLY LOOK ON THE FLOOR
7 operators across 6 stations — every station under takt
Station | Work (SWI steps) | Min/unit
S1 | #2 Connector Prep · #3 Leg Assembly | 27.3
S2 · 2 builders | #4 Arms Assembly (built together) | 32.0
S3 | #5 Seat Frame Assembly (first part) | 41.0
S4 | #5 Seat Frame (rest) · #6 Back Frame (first part) | 39.5
S5 | #6 Back Frame (rest) · #7 Attaching Arms · #8 Back Support · #9 Leg Finishing | 41.0
S6 | #10 Seat Support · #11 Attaching Seat Frame · #12 TUUCI Plate | 41.5
10.1 /day
capacity vs. 10/day demand — met
41.5 min
slowest station (S6) — under takt
88 %
line efficiency (very little idle)
S2 is two builders working Arms together (64 → 32 min). Seat Frame (#5) and Back Frame (#6) are each split across two stations to level the load. Times measured from the SWI.

## Slide 7
TUUCI
Meritage 3-Seater · Summary
7
WHAT THIS MEANS
Same product, leveled to demand
254 min of labor, with 61% in three assemblies — Arms (#4), Seat Frame (#5), Back Frame (#6).
Those three each run longer than takt, so they’re the constraint.
Build Arms 2-up, split Seat & Back Frame, group the rest → 7 operators across 6 stations, every station ≤ 41.5 min.
Result: ~10.1 units/day at 88% efficiency, meeting the 10/day demand.
Assumptions & caveats. Demand 10/day over a 7-hour day → 42-min takt. Times are measured from the SWI. Splitting helps only where a task is genuinely separable; sequence-locked work won’t overlap — to confirm on the floor.
Next step. Validate the three split assemblies on the floor, then trial the 6-station layout. The analyzer re-balances live as real times firm up.