## Slide 1
Sola Lounge No-Arm Standard Work
Douglas O'Keefe
06/18/2026

## Slide 2: Agenda
Review current state standard work procedure
  Cycle Time
  Theoretical Output
  Order of Operations
Operator Loading Chart by Task
Potential Improvements

## Slide 3: Key Takeaways
Sola Lounge (No-Arm) Sofa assembly labor time: 124 min
Theoretical output based on cycle time (36.8 min), assuming parts are available from paint.
  ~11 units per day (4 operators)
  Takt time required (demand of 10 units): 42 min

## Slide 4: Operator Loading Chart by Task
0
12
24
36
48
2
3
4
5
36.8
S1
6
7
34.5
S2
8
33
S3
9
10
20.1
S4
Takt 42 min
Tasks (SWI step #)
#2 Rivet Nut Installation
#3 Connector Pre-Assembly
#4 Connector Plate Installation
#5 Connector Attachment
#6 Frame Sub-Assembly
#7 Frame Connection Assembly
#8 Seat Support Frame Assembly
#9 Trellis Frame Installation
#10 Corner Cap & End Cap
Takt 42 min · Cycle time 36.8 min · Capacity ~11 units/day · 84% line efficiency · Seat Support (#8, 33 min) is the bottleneck — splitting it 2-up unlocks more output.

## Slide 5: Improvements
Balance the line to takt: 4-station layout, every station under the 42-min takt (~11 units/day at ~84% efficiency)
Split the Seat Support / trellis assembly (#8, 33 min) — the bottleneck; multiple slats make it parallelizable, so 2 builders unlock more output
Connectors delivered correct & pre-drilled (Connector Pre-Assembly + Plate + Attachment ≈ 28 min combined) — cut prep and drilling time
Rivet nuts pre-installed by the supplier where possible (Rivet Nut Installation, #2)
Point-of-use storage / kit parts per unit to cut walking and fetching
Standardize cordless tools & batteries and stage a tool set at each station
Clearer quality standards to reduce wait time between assembly and packing approval