## Slide 1
3D Mezzanine Model
Standard-Work Line Simulation
Mac O'Keefe
Continuous Improvement · 07/2026

## Slide 2: Why I built this
We were tasked with creating standard work for the mezzanine lines.
That gave us a lot of good data (station times, people, sequence), but it lived in spreadsheets and SWIs.
I built this simulation as a way to actually see all of that data on the floor, and use it to reach conclusions about optimization.
The goal today: show you what we have, and plan strategies for each line together off the numbers we collected.

## Slide 3: What it is
A 3D model of the mezzanine floor, the real layout, from the CAD drawing.
All three lines run at once, each on its own schedule:
  Meritage, Sola, and Canyon Crew: operators, parts carts, forklifts, and finished-goods flow.
Every station uses the real times from our SWIs.
Live readouts per line: cycle (total labor), current pace, capacity per day, and the bottleneck.
Runs in any browser. No install.

## Slide 4: What we can do with it
Test ideas live and see the effect on pace and output right away:
  Add help where an operator has idle time, and watch the bottleneck station drop.
  Move a step from one station to another to rebalance the line.
  Run different products on a line (Sola sizes, chair vs swivel) and see labor change.
  Focus on one line at a time, or view all three together.
It is a thinking tool for line balancing, not just a picture.

## Slide 5: Where the lines stand today
From the current model, at a 7-hour (420 min) working day:
  Meritage 3-Seater: ~8.6 / day · pace 48.6 min · 272 min labor/unit · bottleneck Seat frame
  Sola Lounge (no arms): 11.0 / day · pace 38.2 min · 168.7 min labor/unit · bottleneck Frame
  Canyon Crew (chair): 14.0 / day · pace 30 min · 99 min labor/unit · bottleneck SWI 10 to 16
These update the moment we change a time, add help, or rebalance, so we can compare options in the room.

## Slide 6: Live look

## Slide 7: What I would like from you
Ideas to try: anything you would want to see run on a line.
Which line should we focus on first for optimization?
A gut-check on the times and assumptions. A few product times are still estimates, not measured SWIs.
Where help between stations is realistic vs where it is not, given how the crews actually work.

## Slide 8: Where this is headed
This is a working tool, not a finished hand-off yet.
Next: move the data to our shared M365 (SharePoint) so a change one person makes updates company-wide.
Keep grounding product times in real SWIs as we collect them.
Longer term: pull layouts straight from CAD so the floor always matches the drawing.