## Slide 1
Meritage 3-Seater Sofa
Engineering Improvement Plan
Douglas O'Keefe
06/18/2026

## Slide 2: Agenda — Meritage 3-Seater (Engineering)
Current state: labor time, cycle time, theoretical output vs. takt
Where the labor goes — the bottleneck steps
Improvement plan (4 engineering fixes)
Deep dive 1 — Connector BOM & pre-assembly (3 real types)
Deep dive 2 — Eliminate connector screw swaps & reorientation
Deep dive 3 — Pre-drill connector holes (seat-frame bottleneck)
Deep dive 4 — Receive leg pieces pre-assembled
Line balance to takt & labor-savings roll-up

## Slide 3: Key Takeaways: Meritage
Meritage 3-Seater Sofa assembly labor time: 254 min (+ 18 min packing for shipping = 272 min total)
Theoretical output based on cycle time (41.5 min), assuming all parts are available.
  ~10 units per day (7 operators)
  Takt time required (demand of 10 units): 42 min

## Slide 4: Where the Labor Goes — Meritage
Total assembly labor: 254 min · + 18 min packing = 272 min/unit
The build is dominated by a few steps — that's where engineering effort pays off:
  Arm assembly — the single largest block of the build (top bottleneck); splittable across operators
  Seat-frame assembly — second bottleneck; gated by leg-piece insertion (no pre-drilled holes)
  Connector work (rivet nut -> pre-assembly -> plate -> attachment) — heavy hand-rework on every unit
Takt for 10 units/day (7-hr day): 42 min/unit
Theoretical output today ~10 units/day at cycle ~41.5 min (7 operators), assuming parts available
Implication: connectors and the seat-frame/leg steps are the highest-leverage targets — all fixable upstream.

## Slide 5: Improvements: Meritage
Assign different connector types part numbers. Currently, the 3 different types of Meritage connectors arrive the same way, and under 1 part #.
Eliminate connector screw swaps & reorientation: recovers ~11:40 of labor per unit to redeploy elsewhere
Pre-drill connector holes for screw entry (for leg piece insertion): saves at least 6 min per frame assembly (seat-frame assembly is a top bottleneck).
Receive leg pieces pre-assembled from manufacturing: There are two types of leg pieces. One of them being used 90% of the time. That one should be outsourced. The only issue is paint.

## Slide 6: First Step to Pre-Assembly: Fix the Connector BOM
The first step to getting connectors pre-assembled in Vietnam: give each connector its own part number in the BOM.
Today all three connectors arrive from Vietnam as one generic type, then get swapped and reconfigured by hand on the line.
The BOM lists 2 connector types — but there are really 3:
Location | Configuration | Part number | Qty
Front of frame | Type 1 (same both sides) | 1015301 | 2
Back – left | Left configuration | 1015302 | 1
Back – right | Right configuration | 1016592 | 1
The gap. Drawings already show all three correctly — 1015301 (×2) front, 1015302 + 1016592 back — but the BOM does not.
The fix. Give each its own part number so it is ordered separately — then every connector arrives from Vietnam already assembled for its specific use (front / back-left / back-right), with no hand reconfiguring on the line.
Note: the Marquesa also uses a specific connector that should be coming pre-assembled — different from the three types covered here.

## Slide 7: Meritage Flat connectors (Classic type #1)
These drawings reflect the engineering teams perspective of the connectors.
In reality, Operator 1 on the floor removes the 40200 screw from every single connector that arrives from Vietnam and replaces it with 1012919 screw.

## Slide 8: Meritage Flat connectors (Type #2 which is split between left and right)
This one comes with 1012934, and the operator currently removes that screw and replaces it with 402014
Half of these also need to have their orientation flipped which seems avoidable. Also, the left and right orientations should have their own part number.

## Slide 9: Meritage Flat connectors (both types)
These drawings reflect the engineering teams current perspective of the connectors.
Operators spend

## Slide 10: Fix 2 — Eliminate Connector Screw Swaps & Reorientation
Problem: every connector arrives from Vietnam as one generic type, so Operator 1 hand-reworks each one before use.
  Type #1 (front, x2): operator removes the 40200 screw and replaces it with 1012919 on every connector.
  Type #2 (back, left/right): arrives with 1012934; operator removes it and replaces with 402014.
  ~Half of Type #2 also need their orientation flipped by hand — avoidable.
Impact: this rework burns ~11 min 40 sec of labor per unit that adds zero value.
Fix: order each connector under its own part number so Vietnam ships it already configured — front / back-left / back-right.
Result: ~11:40 of labor per unit recovered to redeploy onto the bottleneck stations.

## Slide 11: Fix 3 — Pre-Drill Connector Holes for Leg Insertion
Problem: connector holes are not pre-drilled for screw entry, so operators fight leg-piece insertion during seat-frame assembly.
  Seat-frame assembly is a top bottleneck — anything that slows it slows the whole line.
Fix: pre-drill the connector holes (pilot holes for screw entry) before they reach the floor.
Impact: saves at least 6 min per frame assembly, taken directly off the bottleneck.
Because it hits the bottleneck, every minute saved here raises line throughput — not just labor.

## Slide 12: Fix 4 — Receive Leg Pieces Pre-Assembled
Today leg pieces are assembled in-house, adding labor to the seat-frame bottleneck.
There are two types of leg piece; one is used ~90% of the time.
Fix: outsource the high-volume (90%) leg piece pre-assembled from manufacturing.
  Labor in another region is much cheaper than assembling it here — and it removes work from the bottleneck.
Open issue: paint — the pre-assembled leg piece must arrive matching our finish. Resolve before outsourcing.
Action: confirm paint spec / supplier finish capability, then transition the 90% leg piece to pre-assembled supply.

## Slide 13: Line Balance to Takt — Meritage
Goal: every station under the 42-min takt to sustain 10 units/day.
As-built cell: 8 operators, cycle ~47 min (seat-frame bound) -> ~9 units/day — just short of takt.
  Lever 1: add a 2nd operator to seat frame -> cycle ~43.5 (back-frame bound), ~9.7/day.
  Lever 2: add a 2nd operator to back frame -> cycle ~38 min -> ~11/day, clears takt.
The upstream fixes compound: pre-drill + pre-assembled legs shrink the seat-frame bottleneck itself.
Full assembly + packing is self-balancing today (assemble ~29 + pack ~18 = ~47) — packing fills the assemblers' wait time.

## Slide 14: Labor-Savings Roll-Up & Roadmap
Per-unit labor recovered (measured / estimated):
  Connector screw swaps + reorientation: ~11 min 40 sec
  Pre-drill connector holes (seat-frame): >= 6 min
  Pre-assembled leg pieces + pre-assembled connectors: additional, removes steps from the line
Combined: ~18+ min/unit recovered, concentrated on the bottleneck -> directly lifts throughput.
Roadmap:
  1) Fix the connector BOM — give all 3 types their own part numbers (enables everything downstream)
  2) Move connector configuration + the 90% leg piece to pre-assembled supply from Vietnam
  3) Pre-drill connector holes
  4) Re-balance the cell to takt with the recovered labor

## Slide 15: Thank you for your time
Any Questions?